All of the aerosol data submitted has been corrected to Standard Temperature and Pressure (STP), with the exception of absorption,  scattering, and liquid water content (LWC).  See table 1) below for a complete list of submitted variables and whether they have been STP corrected or not.  This correction to STP was done for two main reasons:

- Most gas phase measurements have been submitted as mixing ratios (similar to our STP correction)

- Our instruments are measuring at pressures and temperatures different from ambient conditions (due to RAM pressure increase and sampling at aircraft cabin temperature).

The correction was applied using the formula:

STP data = instrument data*(Standard P/Sample P)*(Sample T/Standard T)

with Standard P=1013 mb and Standard T=298.15 K

This data can then be corrected to ambient conditions using the ambient P and T and the following formula:

Ambient data = STP data*(Ambient P/Standard P)*(Standard T/Ambient T)

with Ambient P and T found in the aircraft data files and merged

data sets

The optical data (absorption and scattering) have not been corrected to STP for historical reasons.  Most uses of aerosol optical data (visibility, radiative forcing, and comparison to remotely measured aerosol properties for example) have required ambient aerosol optical properties, not STP corrected data.  The optical data submitted is not truly at ambient conditions (see (2) above); however, the reported data is very nearly so (within 5%).  To retrieve true ambient optical properties, one must first correct to STP and then correct to ambient conditions.  If one wishes to use STP optical properties (to compare to various gas phase measurements for example), we have included a column in our submitted data that contains a multiplier to correct the reported optical properties to STP.

The liquid water content (LWC) of the air is also not corrected to STP.

Table 1):

Aerosol measurement:                           STP correction applied:                   Submitted data found in:

| CN @ 300 ( C | Yes | tcaerpf##.pmb |
| --- | --- | --- |
| CN @ 30 ( C | Yes | tcaerpf##.pmb |
| Sub-(m scattering @ 3 (’s | No | tcaerpf##.pmb |
| Total scattering @ 3 (’s | No | tcaerpf##.pmb |
| OPC integral number (various cut sizes) @ 30 ( C | Yes | tcopcpf##.pmb |
| OPC integral volume (various cut sizes) @ 30 ( C | Yes | tcopcpf##.pmb |
| OPC integral surface area (various cut sizes) @ 30 ( C | Yes | tcopcpf##.pmb |
| DMA integral number @ 30 ( C | Yes | tcdmapf##.pmb |
| DMA integral volume @ 30 ( C | Yes | tcdmapf##.pmb |
| DMA integral surface area @ 30 ( C | Yes | tcdmapf##.pmb |
| LWC | No | tclwcpf##.pmb |
| Absorption | No | tcabspf##.pmb |

CN = Condensation nuclei concentrations

DMA = Differential mobility analyzer (size distribution measurement with 0.008<=diameter<=0.28 (m)

OPC = Optical particle counter (size distribution measurement with 0.28<=diam<=0.6 (m,            0.6<=diam<=4.0 (m, and 0.28<=diam<=4.0 (m cut sizes)