This tape contains two files of twenty-minute averaged turbulent flux data from 
GTE/ABLE-2b.  The first file, "jungle.001" contains continuous data from        
12:00 (local time) on April 18 to 10:40 on April 30,1987.  The second file,     
"jungle.002", is continuous from 11:00 on April 30 to 08:40 on May 9,1987.  YOU 
MUST CONSULT THE HARDCOPY DOCUMENTATION FOR THIS PROJECT TO FIND OUT WHEN       
INSTRUMENTS WERE ACTUALLY EXPOSED AND WORKING.                                  
                                                                                
For each 20 minute measurement period, there are three data reports,            
identified in the first data field by the number 134, 150 or 217.  These        
reports contain 46,32, and 39 data fields, respectively. Each data field has    
the format:  (I2,F5.4),where the two-digit integer at the beginning of each     
field is the data field number. The data field descriptors for each data        
report are listed below:                                                        
                                                                                
                                                                                
DATA FIELD                                                                      
NUMBER                                                                          
                                                                                
1       134                     150                     217                     
2       Julian date             Julian date             Julian date             
3       hhmm                    hhmm                    hhmm                    
4       ss.ss                   ss.ss                   ss.ss                   
5       mean w1                 sigma-w1                mean w1                 
6       mean t1                 sigma-w2                mean CO2                
7       mean q1                 sigma-w3                mean O3                 
8       mean u                  w1w2                    sigma-w1                
9       sigma-w1                w1w3                    sigma-CO2               
10      sigma-t1                w2w3                    sigma-O3                
11      sigma-q1                sigma-t1                w1CO2                   
12      sigma-u                 sigma-t2                w1O3                    
13      w1t1                    sigma-t3                w1t1                    
14      w1q1                    t1t2                    w1q1                    
15      w1u                     t1t3                    CO2O3                   
16      t1q1                    t2t3                    CO2t1                   
17      mean w2                 sigma-q1                CO2q1                   
18      mean t2                 sigma-q2                O3t1                    
19      mean q2                 sigma-q3                O3q1                    
20      sigma-w2                q1q2                    Julian date             
21      sigma-t2                q1q3                    hhmm                    
22      sigma-q2                q2q3                    ss.ss                   
23      w2t2                    sigma-u(th1)            mean w2                 
24      w2q2                    sigma-u(th2)            mean CO2                
25      t2q2                    sigma-u(th3)            mean O3                 
26      mean w3                 sigma-u                 sigma-w2                
27      mean t3                 u1u2                    sigma-CO2               
28      mean q3                 u1u3                    sigma-O3                
29      sigma-w3                u1u                     w2CO2                   
30      sigma-t3                u2u3                    w2O3                    
31      sigma-q3                u2u                     w2t2                    
32      w3t3                    u3u                     w2q2                    
33      w3q3                                            CO2O3                   
34      t3q3                                            CO2t2                   
35      phi,Gill                                        CO2q2                   
36      mean u(th1)                                     O3t2                    
37      mean u(th2)                                     O3q2                    
38      mean u(th3)                                     xx                      
39      sigma-phi                                       xx                      
40      sigma-u(th1)                                                            
41      sigma-u(th2)                                                            
42      sigma-u(th3)                                                            
43      mean vector wind speed                                                  
44      mean scalar wind speed                                                  
45      mean phi,Gill                                                           
46      sigma-phi,Gill                                                          
                                                                                
W1, t1,q1 refer to vertical velocity, temperature, humidity at level 1 (45      
m).  Levels 2 and 3 for these instruments were 30 and 20 m, respectively.       
The Gill anemometer (wind speed and direction) was located at 45 m.             
Uth1, uth2, uth3 refer to Thornthwaite anemometers at 30m, 25m and 13m.         
Correlations are represented in the table above by pairs of variable names,     
e.g., w2t2 refers to the correlation between w and t at 30 m.  Covariances      
can be recovered by dividing by the sigmas.  Remember that w, t and q are       
obtained from instruments that give only relative measures, so the mean         
values are not significant.  The sigmas for these instruments are in            
units of cm/s, degrees K, and grams per cubic meter.  Values of windspeed for   
the Gill and the Thornthwaites are in cm/s.                                     
                                                                                
        For information concerning calibrations and good operation intervals    
for carbon dioxide (CO2) and ozone (O3), contact:                               
                                                                                
                S. Wofsy                                                        
                Department of Earth and Planetary Sciences                      
                Harvard University                                              
                Cambridge, MA.                                                  
                                                                                
        An additional type of report, identified with 219 in the first field,   
indicates a period when there was a level change in one of the chemical         
instruments.  In these periods, then, a 217 report is immediately followed      
by a 219 report, which has the same field descriptors as the 217.  For all      
reports, missing values are indicated by -99999. A data sample is provided      
below.                                                                          
                                                                                
01+0134.  02+0120.  03+1100.  04+000.2  05-15.886 06-3.5514 07+.01791 08+153.32 
09+43.651 10+.22303 11+.30459 12+72.542 13+.52178 14+.52516 15-.31195 16+.59925 
17+103.93 18-3.9760 19+.08605 20+36.388 21+.28167 22+.19401 23+.41812 24-.16272 
25-.12960 26+103.16 27-1.9860 28+.01782 29+18.114 30+.24621 31+.49787 32-.15473 
33+.14565 34-.50784 35+63.252 36+15.873 37+22.191 38+68.738 39+72.267 40+25.662 
41+39.243 42+77.020 43+153.32 44+137.94 45+44.003 46+25.651                     
01+0150.  02+0120.  03+1100.  04+000.7  05+43.651 06+36.388 07+18.114 08+.50060 
09+.51187 10+.53435 11+.22303 12+.28167 13+.24621 14+.31599 15-.00766 16-.00569 
17+.30459 18+.19401 19+.49787 20+.00966 21+.11563 22-.39553 23+25.662 24+39.243 
25+77.020 26+72.542 27-.02678 28+.05458 29+.05745 30+.10069 31+.08083 32+.24573 
01+0217.  02+0120.  03+1100.  04+001.3  05-12.285 06+1690.6 07+9.4700 08+44.419 
09+64.141 10+87.902 11-.05927 12-.02152 13+.55045 14+.56494 15-.29514 16-.17966 
17-.16988 18-.05693 19-.02584 20+0120.  21+1100.  22+001.6  23+103.47 24+1690.6 
25+9.4700 26+35.971 27+64.141 28+87.902 29-.18524 30-.01999 31+.41162 32-.15733 
33-.29514 34-.19337 35+.20854 36+.01139 37-.09799 38+3022.7 39+150.00