CITE3 MISSION
                          FLIGHTS 04 THRU 21
                      AUGUST THRU SEPTEMBER 1989
                        OZONE AND AEROSOL DATA
                          G. L. GREGORY, PI

    The accompanying diskettes contain 10 second averages of ozone and aerosol
measurements from an ethylene chemiluminescence ozone detector and two Particle
Measuring Systems aerosol probes, respectively, taken during the CITE3
aircraft missions.  The data have been edited to exclude errant points;
those with a value of -9999.0 indicate bad or missing data or that a
break exists in the time series.  The data is stored in ASCII format and can 
be directly inputted into lotus or similar spread sheet programs.

   Aerosol size distributions are not included in this data set but are
available through the CITE3 data archive on high density 5.25" floppy disks,
one disk per flight.

   The first line of each file contains the following header denoting
the data organization within the file:

hr mn sc     alt      O3       npcca     npccb     %ch1b

where:

hr mn sc - Universal time at the midpoint of the 10 second average,
     alt - average pressure altitude in feet,
      O3 - ozone mixing ratio in ppb,
   npcca - average counts/sec*cm3 from the large (0.5-8.0 um) aerosol probe,
   npccb - average counts/sec*cm3 from the small (0.12-0.312 um) aerosol probe,
   %ch1b - percentage of small aerosol counts occuring in size bin 1,
           (0.125 - 0.15 um diameter)

    File names have the format "c3fnn.glg", where nn is the flight number
and the extension, ".glg" identifies the data as that from G.L. Gregory's
instrumentation.  When more than one leg was flown per mission, as in the
ferry flights, the files are further identified by adding an a or b to the
flight number.
    Aerosol data does not exist for flights 20 and 21 and occasionally data are
missing for other flights as well.  Table 1 identifies the time periods
when data were recorded and provides information on data validity.


TABLE 1.  Data Summary
_______________________________________________________________________________
Flight    Date       Start       End                     Comments
-------------------------------------------------------------------------------
  4     22Aug89    15:12:15   21:08:55     No aerosol data for the first 
                                           two minutes of flight.

  5     23Aug89    15:14:45   20:53:55 

  6     25Aug89    14:22:05   19:59:35     Invalid data at 16:24:35, 17:20:35,
                                           & 17:22:25.

  7     28Aug89    14:51:35   20:52:35     No aerosol data for first 20 seconds
                                           Invalid data at 16:41-16:42.

  8     30Aug89    15:16:45   21:21:15     No aerosol data for first 20 seconds

  9     31Aug89    15:23:45   21:15:35     First aerosol record invalid

 10     1Sept89    14:55:15   20:17:55          

 11_1   8Sept89    12:41:15   17:58:55 

 11_2   8Sept89    19:09:45   21:20:05     First 20 seconds of aerosols invalid

 12_1   9Sept89    12:02:05   14:54:14     First 20 seconds of aerosols invalid

 12_2   9Sept89    16:07:15   21:11:55     First 20 seconds of aerosols invalid

 13    12Sept89    11:52:15   17:53:15  

 14    15Sept89    13:58:15   19:37:05

 15    16Sept89    02:59:25   08:33:15     First aerosol record invalid

 16    19Sept89    14:02:15   19:56:03     First 20 seconds of aerosols invalid

 17    20Sept89    03:01:05   08:30:35     Invalid large aerosols @ 03:04:25 &
                                           05:58:15.

 18    22Sept89    06:58:05   12:40:55    First aerosol record invalid; Probe B
                                          data invalid before 07:03:35.

 19    22Sept89    15:33:35   21:18:35    

 20a   28Sept89    12:35:45   16:45:25     No aerosol data!

 20b   28Sept89    18:05:35   20:21:25     No aerosol data!

 21a   29Sept89    12:52:55   18:32:45     No aerosol data!

 21b   29Sept89    20:19:05   22:44:25     No aerosol data!
-------------------------------------------------------------------------------